## Slide 1: Cal Poly SLO Hyperloop Propulsion CDR
Syed Huzefa Rauf & Kent Roberts

## Slide 2: Propellant Selection
Gas | Molecular Weight | Specific Impulse (sec) | ∝ Total Impulse per unit Volume
Air | 28.9 | 74 | 2138.6
Argon | 39.9 | 57 | 2274.3
CO2 | 44 | 67 | 2948
Helium | 4 | 179 | 716
Hydrogen | 2 | 296 | 592
Nitrogen | 28 | 80 | 2240
Methane | 16 | 114 | 1824
Air is widely available for a test campaign, performance runs where T<0°C, use nitrogen

## Slide 3: Rocket Equation
mf=Inert Pod Mass (Non-Tank Pod mass + Tank Mass + Residual propellant)
m0=Wet Pod Mass (mf + Propellant Mass)

## Slide 4: Isentropic Processes and Tank Discharge Limitations
T2=Lower Temperature Limit of the Tank
P2=Lower Pressure Limit (function of Pnozzle_Inlet and Flow Coefficient of Hardware Cv)

## Slide 5: Rocket Eq. & Isentropic Process
Use the Ideal Gas Law to find ρ1

## Slide 6: Final Mass, Pod Class

## Slide 7: Valve Requirements
Inlet Pressure ~4800psi
  ~ASME Class 2500