## Slide 1: Cal Poly SLO Hyperloop Propulsion CDR
Kent Roberts & Syed Huzefa Rauf

## Slide 2: Propellant Selection
Gas | Molecular Weight | Specific Impulse (sec) | ∝ Total Impulse per unit Volume
Air | 28.9 | 74 | 2138.6
Argon | 39.9 | 57 | 2274.3
CO2 | 44 | 67 | 2948
Helium | 4 | 179 | 716
Hydrogen | 2 | 296 | 592
Nitrogen | 28 | 80 | 2240
Methane | 16 | 114 | 1824
Air is widely available for a test campaign, performance runs where T<0°C, use nitrogen

## Slide 3: Rocket Equation
mf=Inert Pod Mass (Non-Tank Pod mass + Tank Mass + Residual propellant)
m0=Wet Pod Mass (mf + Propellant Mass)

## Slide 4: Isentropic Processes and Tank Discharge Limitations
T2=Lower Temperature Limit of the Tank & Valve hardware
P2=Lower Pressure Limit (function of Pnozzle_Inlet and Flow Coefficient of Hardware Cv)
*Most systems with T2~-40F and P2~500psi are Temperature limited

## Slide 5: Rocket Eq. & Isentropic Process
Use the Ideal Gas Law to find ρ1

## Slide 6: ΔV as a Function of Pod Inert Mass and Tank Specifications

## Slide 7: Pod Inert mass as a function of ΔV and Tank Specifications

## Slide 8: Pod Inert Mass v. Tank System ΔV=500km/hr
Values Below 0 implies that the velocity (500km/hr) is unobtainable with the given tank system

## Slide 9: ΔV v. Tank System mInertPod=322[lb]
Goal
Current Record
[463.5 km/hr]
(WARR)
Swissloop
[257 km/hr]
2019 2nd

## Slide 10: Tank Dimensions
Generally, tank systems were only considered if they were within reasonable dimensions
For a more detailed breakdown, reference the google sheet document.
An initial design is further presented with the 2X10070504-2 configuration and a 2 X SH 90 alternative (Former sourced from General Dynamics, later from Steelhead Composites)
  10070504-2 [15.2in⌀ X 42.3in]
  SH 90 [17.1in⌀ X 39in]

## Slide 11: 2 X10070504-2 CAD
This is to demonstrate general dimensions; the flow schematic shall be discussed later.
2 X SH 90 Configuration would share similar dimensions

## Slide 13: Mass Flow Rate
Assume a constant flow rate

## Slide 14: 2 X10070504-2 Mass Flow Rate
322 lb Inert Pod mass, 600m thrusting length, 377 km/hr max v
Coast/Braking =>

## Slide 15: Nozzle Design
Configuration options:
Tank
Straight dump
Phase through Under/Over expanded
No pressure regulation
Dynamics?
Aerospike
Variable expansion
No pressure regulator
Thermal
Manufacturing
Cool factor
Tank
Regulated
Optimal expansion
Requires pressure regulation
Additional set of nozzles for testing
Tank
Tank
Dual-Bell
One nozzle with optimal expansion for the tube & 1atm testing
Requires pressure regulation
Notes: Dual-Bell operational advantage, test at 1 atm, system will preform predicable, go straight to test without disassembling the high-pressure system (and draining/refilling the tanks <- takes time (ISOTHERMAL))

## Slide 16: Nozzle Design
The nozzle mass flow rate must be above the physics requirement (to accelerate within the thrust length) and within the limits of the flow hardware
Avoid the possibility of supersonic flow in the hardware
Notes: Dual-Bell operational advantage

## Slide 17: Nozzle Design
Minimum orifice
2 X 10070504-2 System (322lb):
This is for a combination of extrema of P_1 and T_1, a condition which is not predicted. (a more refined approach will be implemented later)
Notes: Dual-Bell operational advantage

## Slide 18
Tank 2 X 10070504-2
[p0=4800psi]
S
M
Manual Relief
Control Relief
Relief Pressure
Regulator
TESCOM BB13AL2?B?
Manual Valve
(Close during fill & Prior to operation)
Flow-Tek Triad Models HP
1” Cv = 32
Primary Control Valve
Flow-Tek Triad Models HP
1” Cv = 32
V-Port Ball?
S70 Electric Actuator?
Default Closed
Pressure Regulator (Diaphragm)
TESCOM 26-1200
1/2” MS33649 Cv = 3.3
Nozzle(s)
Low Pressure Diaphragm Reference System
High Pressure Fill
Low Pressure Relief
Safety Relief
Safety Relief
4800psi
~125psi
270psi
P
T
T
P
Safety Relief
P
270psi
Pilot Pressure Reg.
TESCOM BB13AH1?B?